## Slide 1: Deep decarbonisation of the Dutch heavy industry through electrification of the production of basic materials and transportation fuels
Toon van Harmelen, Clemens Schneider, Yvonne van Delft, Robert de Kler, Mathieu Baas, Vincent Kamphuis

## Slide 2: Key Findings
Three what-if electrification scenarios demonstrate that reduction of life cycle CO2 emissions to near 0 in 2050 is technically possible;
Required renewable electricity potentials are large: 1,5 – 2,5 times the Dutch North sea wind energy potential;
Life cycle CO2 emissions of heavy industry and transport are comparable to total Dutch GHG emissions (219 Mt CO2 eq);
Two scenarios, All electric and Big on hydrogen, show possibilities for fossil fuel independence. The Competition scenario shows the possibilities while relying partly on conventional technology with CCS;
Each scenario needs its own infrastructure with its challenges;
A favourable scenario is likely a combination.

## Slide 3: Content
Objective
Approach & model set-up
Methodology & assumptions
Three what-if electrification scenarios
Results
Conclusions & recommendations

## Slide 4: Objective
To explore deep decarbonisation scenarios for the demand of the Dutch heavy industry in 2050, through electrification of the production of basic materials and transportation fuels
identify the technical feasibility,
required feedstock and energy potentials and
pros and cons of different electrification pathways

## Slide 5: Approach
Inventory of current and future situation
Inventory of options
Design of scenarios
Model calculations
Iterative discussions
Reporting

## Slide 6: Model set-up
Based upon: Decarbonising the energy intensive basic materials industry through electrification - Implications for future EU electricity demand, Stefan Lechtenböhmer et al (2015, Wuppertal Institute & Univ of Lund)
Calculation model
Input
Production levels of basic materials, fuels, food and paper (2010, 2050)
Production technology (2010, 2050)
Energymix (2010, 2050)
Carbon resources
Renewable energy potential
Output
Energy demand of production process (electricity, H2, syngas/FT-naphta)
Feedstock demand (carbon and fuel) of production process (H2, CO2, syngas/FT-naphta)
Direct CO2
Indirect CO2
Parameters
Energy/production [TWh/Mton]
Feedstock/production [TWh/Mton]
Direct CO2/production [Mton/Mton]
Indirect CO2/production (energy, carbon feedstock, combustion of fuels, end-of-life) [Mton CO2-eq/Mton]

## Slide 7: Methodology & assumptions
Life cycle CO2 to 0: direct fossil based CO2 emissions at production, use phase, end-of-life of products (also of exports)
What-if electrification scenarios sketching three distinct technology based pathways
Modest volume growth, no structural changes (“High growth” scenario from Prosperity & environment, CPB/PBL 2015)
Using North Sea wind power potentials, incl. 23% battery storage losses for maintaining security of supply:
  NL: 34 GW ~ 130 TWh (PBL, 2011)
  North Sea: 250 GW ~ 1000 TWh (Energy Odessey)
  90% one-way battery efficiency (projected battery efficiency, TNO 2018)

## Slide 8: Domestic use and export
Currently, refineries and chemical industry produce approximately ¼ for the domestic and ¾ for foreign markets;
In scenarios for 2050, the chemical industry is assumed to maintain its production of mainly plastics for the foreign market;
In scenarios for 2050, transport fuel for export and international bunkers (navigation and aviation) is assumed to be disappeared (electricity, hydrogen or biomass is not supplied from the Netherlands);
For a clear analysis, the same assumption is applied for both the current situation as the 2050 scenarios.

## Slide 9: Three what-if electrification scenarios

## Slide 10: Scenarios: leading indicators
Scenario All electric & Big on hydrogen
Scenario Competition
Current situation
This study: Deep decarbonisation
Indicators give insight in the transition process towards electrification. Based on the TNO study “Electrification options for the Port of Rotterdam”, a case study for Smart Port by Robert de Kler et al. 2017

## Slide 11: Current situation
Carbon source
Energy source
Industry
Products & Markets
Products
Basic Chemicals
  Olefins
  Ammonia
  Chlorine
Metal
  Iron & steel
  Aluminum
Food
Minerals
  Glass & ceramics
  Cement
Paper & pulp
Transport Fuels
  Road Transport
  Aviation
  Navigation
fossil
CO2
Current
CO2
CO2
CO2

## Slide 12: What-if scenarios A, B and C
H2
Carbon source
Energy source
Industry
Products & Markets
All Electric
waste
bio
H2
bio
Big on hydrogen
waste
H2
fossil
CO2
bio
Competition
CCS
CCS

## Slide 13: What-if scenarios: Three distinct technological pathways
Scenario | Current situation | A. All electric | B. Big on hydrogen | C. Competition
Short description | Production is largely fossil based | Renewable electricity as energy carrier in industry and transport. Maximal direct electrification with storage issues. Refineries are closed | Hydrogen as final energy carrier for transportation and industry, produced with conversion losses by renewable electricity. Refineries are closed. Add H2 infrastructure | A mix of energy carriers, renewable electricity (indirect electrification, hydrogen), fossil fuels with CCS and bio(syn)fuels. Add CO2 infrastructure
Carbon source and CO2 emissions | Fossil based energy and feedstock, high CO2 emissions | Partly closed carbon cycle, waste & bio (growth) used as feedstock (olefins), near zero CO2 emissions | Partly closed carbon cycle, waste & bio (growth) used as feedstock (olefins), near zero CO2 emissions | Crude oil for olefins and coal for steel combined with CCS; scarce bio based synfuels used for transportation and small sectors, near zero CO2 emissions
Leading stakeholders | Gas and petrochemical industry | Power sector (DC grid) | Gas sector (H2 grid) | Petrochemical industry and others
Demand projection | Product and service demand projections are from the PBL scenario high growth, combined with assumed high energy efficiency improvements up to a factor 2 |  |  | 

## Slide 14: Technological options by subsector and scenario
Sector | Subsector | Product | Processes |  |  | 
 |  |  | Current situation | A. All electric | B. Big on hydrogen | C. Competition
Basic chemicals | Olefins (High Value Chemicals) | Ethylene, propylene, other | Current crude oil based processes | Bio (for export) and waste (domestic) based MTO/MTA are used for olefin production | Bio (for export) and waste (domestic) based MTO/MTA are used for olefin production | Use crude oil refining and naphta and gasoil steam cracking and residue gasification via MTO to produce olefins/aromatics (CCS waste incineration)
 | Chlorine |  | Current electrical process | Current electrical process | Current electrical process | Current electrical process
 | Ammonia | Fertilizer | Current natural gas based processes | Direct electrical ammonia synthesis | Indirect electrical ammonia synthesis via H2 | Current gas based, decarbon electricity + CCS
Transport | Freight road | Diesel | Combustion engines | Electric vehicles | H2 fuel cells | Biobased syndiesel or OME
 | Passenger road | Gasoline, diesel, CNG and electricity | Combustion engines | Electric vehicles | H2 fuel cells | Biobased syndiesel or OME
 | Aviation | Kerosene | Combustion engines | Electric airplanes | H2 fuel cells | Biobased kerosene
Oil refinery | Basic chemicals |  | Crude oil refining | None | None | Crude oil for feedstock
 | Fuels |  | Crude oil refining | None | None | None
Metal | Iron & steel: | Primary steel | Blast oxygen furnace | Electrowinning | Direct reduction H2 + EAF | HISARNA or TGR + Carbon Capture
 |  | Secondary steel | EAF, Secondary steel from scrap | EAF, Secondary steel from scrap | EAF, Secondary steel from scrap | EAF, Secondary steel from scrap + CCS
 | Aluminium |  | Current process | Current process | Current process | Current process
Minerals | Glass | Container glass, flat glass, glass fibre | Current processes | Electric oven | H2 oven | Synthetic CH4 oven + CCS
 | Cement | Cement | ENCI | None | None | None
 | Lime | Lime | No lime production | None | None | None
Food |  | Milk powder, potato & sugar represent sector | Steam boilers | Heat pumps + compression + HT storage, breakthroughs | Heat pumps + compression + H2/fuel cells, fuel mix change | Biogas BAT, decarbon electricity
Paper & pulp |  | Paper | Steam boilers | Heat pumps + compression + HT storage, breakthroughs | Heat pumps + compression + H2/fuel cells, fuel mix change | Biogas BAT, decarbon electricity

## Slide 15: Results

## Slide 16: Current domestic CO2 emissions (2010)
Chart: 
 | 42 | 50 | 55 | 58 | 60
 | 42 | 8 | 5 | 3 | 2 | 38 | 25
 | 34
 | 6
 | 33
 | 0
Transport Fuels
End of Life CO2 emissions
Direct Process CO2 emissions
Use phase CO2 emissions
Electricity CO2 emissions
Total
CO2 emissions [Mton]
98
6
Metal
Basic Chemicals
5
3
Minerals
Food
Paper & pulp
2
Basic chemicals (incl. export) and transport (excl. export) are dominant

## Slide 17: Current CO2 including exported fuels
Chart: 
 | 25 | 0
 | 6 | 0
 | 34 | 110
 | 33 | 14
CO2 emissions [Mton]
0
0
124
6
Current Domestic
Current Export
98
Use Phase CO2 emissions
Direct Process CO2 emissions
End of Life CO2 emissions
Electricity CO2 emissions
Current CO2 of industrial life cycle are comparable to total Dutch GHG emission (219 Mton)

## Slide 18: Current situation
Chart: 
 | 644 | 747 | 819 | 849 | 877
 | 644 | 103 | 72 | 30 | 28 | 506 | 52
 | 857
 | 474
 | 0
Metal
30
Food
Basic Chemicals
Minerals
28
Paper & pulp
Fossil fuel
Fossil feedstock
Total
1.383
52
Transport Fuels
Fossil based electricity
1.400
Energy Demand [PJ]
Energy and feedstocks almost completely fossil based

## Slide 19: 2050 Scenario All electric
Chart: 
 | 682 | 760 | 820 | 850 | 882
 | 682 | 78 | 60 | 30 | 32 | 190 | 820
 | 229
 | 23
 | 0
60
Basic Chemicals
Food
Metal
Renewable Electricity
32
Total
Paper & pulp
Waste feedstock
Biomass feedstock
23
1.072
Minerals
30
Energy Demand [PJ]
1.400
Transport Fuels
Direct electricity reduces energy demand with 20%; 2x NL North Sea wind, 25% total NS;
completely fossil independent

## Slide 20: 2050 Scenario Big on hydrogen
Chart: 
 | 677 | 863 | 934 | 973 | 1012
 | 677 | 186 | 71 | 39 | 39 | 326 | 1085
 | 229
 | 23
 | 1
1.400
Transport Fuels
Basic Chemicals
Energy Demand [PJ]
23
Paper & pulp
39
Minerals
39
Metal
Food
Biomass feedstock
Renewable Electricity
Total
1.338
Waste feedstock
Indirect electricity via hydrogen results in a more or less stable energy demand, completely fossil independent

## Slide 21: 2050 Scenario Competition
Chart: 
 | 615 | 737 | 787 | 821 | 851
 | 615 | 122 | 50 | 34 | 30 | 1000 | -1
 | 762
 | 468
 | 181
 | 441
1.200
500
400
300
1.100
200
100
0
900
1.900
800
700
600
1.800
1.300
1.000
1.400
2.000
1.600
1.500
1.700
Renewable Electricity
Fossil feedstock
Energy Demand [PJ]
Transport Fuels
1.400
Minerals
30
Basic Chemicals
1.851
34
Paper & pulp
Food
Metal
Total
50
Fossil fuel + CCS
Biomass fuel
Increase of energy demand with 30%; biomass potential ~ 2 x NL; same electricity potential; crude oil and CCS needed

## Slide 22: 2050 Primary energy demand
Chart: 
 | 109 | 18 | 11
 | 712 | 1067 | 750
 | 52
 | 1613 | 1332 | 649
 | 229 | 229
 | 23 | 23 | 441
Competition
1.337
Current (export)
1.073
1.384
1.851
Current (domestic)
Big on Hydrogen
All Electric
Energy Demand [PJ]
Security of supply Renewable electricity
Waste feedstock
Fossil based electricity
Renewable electricity
Fossil fuel & feedstock
Biomass fuel & feedstock
North Sea wind potentials needed up to 2,5x NL North Sea wind, 30% total NS;
C fossil dependent, biomass potential 2x NL

## Slide 23: 2050 Primary energy demand per sector
Chart: 
 | 645 | 683 | 676 | 615
 | 103 | 78 | 186 | 122
 | 72 | 60 | 71 | 50
 | 30 | 30 | 39 | 34
 | 28 | 32 | 39 | 30
 | 1613 | 506 | 190 | 326 | 1000
Current (export)
1.384
All Electric
1.073
Current (domestic)
1.851
Big on Hydrogen
Energy Demand [PJ]
Competition
1.337
Minerals
Basic Chemical
Metal
Food
Transport Fuels
Paper & Pulp
Sweet spots: All electric based transport & steel, Big on hydrogen based basic chemicals

## Slide 24: Conclusions & recommendations

## Slide 25: Conclusions
It is technically possible to reduce life cycle CO2 emissions to near 0 in the what-if scenarios All electric, Big on hydrogen and Competition in 2050;
Current life cycle CO2 emissions of the Dutch energy intensive industry & transport are comparable to the current total of Dutch direct GHG emissions (219 Mton);
Required renewable electricity potentials are large: 1,5 – 2,5 times the Dutch North sea wind energy potential, equalling 20% - 35% of the total North sea wind potential;
Energy use is comparable to the current situation in scenario Big on hydrogen, 20% lower in All electric and 30% higher in Competition (mainly due to transport);
Two scenarios, All electric and Big on hydrogen, show possibilities for fossil fuel independence. The Competition scenario shows the possibilities while relying partly on conventional technology with CCS;
Carbon sourcing in scenario A & B requires limited biomass potentials (10% of the Netherlands area) for plastic production growth, while in scenario C required potentials are large for transport (biomass potentials of 2x the Netherlands area) and fossil fuels for plastics;
Each scenario needs its own infrastructure and has its own challenges (storage, transport, safety);
A favourable scenario is likely a combination of different scenario elements applied in different markets / sectors: A. direct electrification in transport, steel & minerals; B. hydrogen in basic chemicals; C. renewable alternatives in food & paper.

## Slide 26: Recommendations for further work
Further investigate:
How to prepare the next decade for potential long term scenarios – identify critical & no-regret technologies, in general and per sector & product;
Economic impacts and feasibility – for value chain and Dutch society;
Necessary governance to support desired developments;
Dutch export position on future decarbonised energy carriers for transportation (aviation and navigation) - currently 3x the domestic use.